## Slide 1: Lecture 5 – Network Layer and IP Addressing
COMP1002 (Cybersecurity and Networks)

## Slide 2: Overview
Network layer (CCNA1 - ch8)
  The role of the Network layer - describe communication from one end device to another end device.
  Internet Protocol (IP) and its features for providing connectionless and best-effort service.
Basic router configuration (ch10)
IPv4 addressing (ch11)
  The division, or grouping, of devices into networks.
  Hierarchical addressing of devices and how this allows communication between networks.
  The fundamentals of routes, next-hop addresses, and packet forwarding to a destination network.

## Slide 3: Part 1: Network Layer

## Slide 4: Aim and objectives
Aim: the Network layer (OSI Layer 3) provides services to exchange the individual pieces of data over the network between identified end devices.
Basic processes:
  Addressing
  Encapsulation
  Routing
  Decapsulation

## Slide 5: Processes
Addressing – provided addresses must be unique
Encapsulation – add src/dst address to each network layer PDU (packet)
Routing - provide services to direct the packets to their destination host
Decapsulation – extract content of the packet at the destination host

## Slide 6: Protocols
Internet Protocol version 4 (IPv4)
Internet Protocol version 6 (IPv6)

## Slide 7: IPv4
RFC791 – September 1981
The standard for the current Internet
  IPv6 - only isolated and encapsulated in IPv4
IP - low overhead, only delivery of packets from source to destination over an interconnected network(s).
Characteristics
  Connectionless - No connection is established before sending data packets.
  Best Effort (unreliable) - No overhead is used to guarantee packet delivery.
  Media Independent - Operates independently of the medium carrying the data.

## Slide 8: Characteristics
Connectionless service = no prior notification of the recipient
  No confirmation of arrival
  Therefore, IP has:
    No additional control fields in header
    No control data
    No knowledge of end-to-end delivery
Media independence = no specific requirements for the link layer
  No strict packet size
  No single transport medium
Best effort = No reliability
  No guarantees about delivery
  No capability to manage or recover from loss
  Therefore, IP has no control fields in the header and no packet tracking

## Slide 9: IPv4 header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| IHL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Options | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Notes: IHL: Internet Header Length. What is the minimum length of IPv4 header?

## Slide 10: IPv4 fields
IP Source / Destination Address (32b)
Time-to-Live (TTL) (8b) - the remaining "life" of the packet.
  Decreased by at least one each time the packet is processed by a router
  When the value becomes zero, the router discards or drops the packet and it is removed from the network data flow.
  This mechanism prevents routing loops

## Slide 11: IPv4 fields (cont)
Protocol (8b) - data payload type
  Enables Network layer to pass data to appropriate upper-layer protocol.
  e.g.: 01 ICMP, 06 TCP, 17 UDP
Type-of-Service (TOS) (8b) – priority
  To be used by Quality-of-Service (QoS)
Fragment Offset (13b)
  Router may fragment a packet when forwarding it from one medium to another medium that has a smaller MTU.
  IPv4 uses Fragment Offset and the MF flag to reconstruct the packet at the destination host.
More Fragments (MF) flag – (1b)
  MF=1 - not the last fragment of a packet.
  MF=0 – last fragment of a packet, reconstruct
Don't Fragment flag
  DF=1 – fragmentation is not allowed
Notes: MTU: maximum transmission unit. For Ethernet, MTU is 1500 bytes.

## Slide 12: Transport across networks
If communication is between hosts in different networks, the local network delivers the packet from the source to its gateway router
Router examines the network portion of destination address and forwards the packet to the appropriate interface.
  If destination network is directly connected, the packet is forwarded directly to that host.
  If the destination network is not directly connected, the packet is forwarded to a second router (next-hop router)
At each hop, the forwarding decisions are based on the information in the IP packet header

## Slide 13: Routing
No packet can be forwarded without a route - the device must have a route to identify where to forward the packet.
A host must either forward a packet to the host on the local network or to the gateway, as appropriate
  The host must have routes that represent these destinations.
A router makes a forwarding decision for each packet that arrives at the gateway interface.
  This forwarding process is referred to as routing.
The destination network may be a number of routers or hops away from the gateway.
  The route only indicates the next-hop router, not the final router.

## Slide 14: Forwarding process
Routing - packet-by-packet and hop-by-hop.
Each packet is treated independently in each router along the path.
  Examine destination IP address and check routing table for forwarding information.
The router will either:
  Forward packet to the next-hop router
  Forward packet to the destination host
  Drop packet

## Slide 15: Using the gateway

## Slide 16: IPv4 routing table – host

## Slide 17: IPv4 routing table – host
Network Destination - reachable networks.
Netmask - determine the network and the host portions of the IP address.
Gateway - address used by the local computer to get to a remote network destination. If a destination is directly reachable, it will show as “on-link” in this column.
Interface - address of the physical interface used to send the packet to the gateway that is used to reach the network destination.
Metric - cost of each route and is used to determine the best route to a destination.
Notes: For a host, it can receive the default gateway address from DHCP (Dynamic Host Configuration Protocol) or configure manually.

## Slide 18: IPv4 routing table - host
0.0.0.0 - default route
127.0.0.0 – 127.255.255.255 – loopback
192.168.10.0 - 192.168.10.255 – local network
  192.168.10.0 - The local network route address
  192.168.10.10 - The address of the local host.
  192.168.10.255 - The network broadcast address
224.0.0.0 - multicast class D addresses
255.255.255.255 – limited broadcast IP address values for loopback interface (127.0.0.1) or the host IP address (192.168.10.10)

## Slide 19: Routing tables

## Slide 20: Routing table - router
Directly-connected routes – from active router interfaces.
  Added when an interface is configured/activated with an IP address
Remote routes - from remote networks connected to other routers.
  Either be manually configured on the local router by the network administrator or dynamically configured by enabling the local router to exchange routing information with other routers using dynamic routing protocols.

## Slide 21: Routing table - router

## Slide 22: Routing table - router
Directly connected interfaces
  C - directly connected network, automatically created when an interface is configured with an IP address and activated.
  L - link local route, automatically created when an interface is configured with an IP address and activated.
Remote networks
  S - route was manually created by an administrator to reach a specific network. This is known as a static route.
  D - route was learned dynamically from another router using the Enhanced Interior Gateway Routing Protocol (EIGRP).
  O - route was learned dynamically from another router using the Open Shortest Path First (OSPF) routing protocol.

## Slide 23: Routing table – router
Route source - Identifies how the route was learned.
Destination network - Identifies the address of the remote network.
Administrative distance - Identifies the trustworthiness of the route source.
Metric - value assigned to reach the remote network - lower values indicate preferred routes.
Next-hop - Identifies the IP address of the next router to forward the packet.
Route timestamp - Identifies when the route was last heard from
Outgoing interface - exit interface to forward a packet to final destination.

## Slide 24: Routing examples
PC1 to 192.168.10.1
PC1 to 192.168.11.10
PC1 to 209.165.200.226
PC1 to 10.1.1.10

## Slide 25: IOS
Internetworking Operating System
  used by Cisco in its routers
Certain models include a GUI, but typical configuration is done via CLI
At boot:
  startup-config (NVRAM) is copied into RAM and stored as the running-config file.
  IOS executes running-config.
  Any changes are stored in running-config and are immediately implemented by the IOS
Notes: Non-Volatile RAM: the data will not be lost when power down.

## Slide 26: Interfaces
Management ports
  Console port – serial communication
  Auxiliary port – similar to console, also modem
Network ports
  LAN - Ethernet/Fast Ethernet
  Enhanced high-speed WAN interface card (EHWIC) slots - provide modularity and flexibility by enabling the router to support different types of interface modules, including Serial, digital subscriber line (DSL), switch port, and wireless.

## Slide 27: Interfaces

## Slide 28: Boot process
Notes: POST: power on self test

## Slide 29: Boot process
Performing POST (Power On Self Test)
  Test router hardware
Loading the bootstrap program
  Copy bootstrap from ROM to RAM and execute
Locate and load the Cisco IOS software
  IOS can be stored on flash, tftp server, etc
  Copy/extract IOS from flash into RAM
Locate and load startup configuration
  NVRAM, tftp server,etc
  If not found – router may go into setup mode
CLI (Command Line Interface)
The content of the router may be seen using the show version command

## Slide 30: Routing process
Router examines the destination IP of each received packet and decides what to do with it based on a routing table
  Match found
    Directly connected to the network – send the packet to destination
    Not directly connected – forward it to another router
  No match found – drop the packet
Routing – layer 3 (based on IP addresses)
  Routers operate at layers 1,2, and 3

## Slide 31: Basic router configuration

## Slide 32: Interface configuration

## Slide 33: View/verify configuration
View running/startup config
  R1#show running-config
  R1#show startup-config
Copy running config to startup config
  R1#copy running-config startup-config
View current routing table and interface status
  R1#show ip route
  R1#show interfaces
  R1#show ip interface brief

## Slide 34: Configure default gateway
Host
  Part of the interface configuration
Switch
S1(config)# interface vlan1
S1(config-vlan)# ip address 192.168.10.50 255.255.255.0
S1(config-vlan)# no shut
S1(config)# ip default-gateway 192.168.10.1

## Slide 35: Summary
Network layer – carry data over the network
  Routing table – core/essential
IPv4
Default gateway – connecting the network with the rest of the internet/Internet
Router architecture – CPU, memory, storage, interfaces
Basic configuration of a router

## Slide 36: Lab activities
10.1.4 – Configure initial router settings

## Slide 37: Go to www.menti.com and use the code 5652 3480

## Slide 38: Part 2: IP Addressing

## Slide 39: Overview
Explain the structure IP addressing
Classify IPv4 addresses by type
Explain how IP address are assigned to networks
Determine the network portion of the host address and explain the role of the subnet mask in dividing networks.
Calculate the appropriate addressing components, given IPv4 addressing information and design criteria,.
Use common testing utilities to verify and test network connectivity and operational status of the IP protocol stack on a host.

## Slide 40: Representation
Binary (as in IP header)
  10101100000100000000010000010100
Dotted decimal
  172.16.4.20
Network and host portion (for a /16 netmask)
  172.16.4.20

## Slide 41: Binary-decimal conversion
The number: 245
  a.k.a. 11110101
  (a.k.a. f5)
Decimal representation
  245 = 2102 + 4101 + 5100
Binary representation
11110101 = 127 + 126 + 125 + 124 + 023 + 122 + 021 + 120
  = 128 + 64 + 32 + 16 + 4 + 1

## Slide 42: Binary-decimal conversion (cont)

## Slide 43: Binary-decimal conversion (cont)

## Slide 44: Binary-decimal conversion (cont)

## Slide 45: Addresses within a (sub)net
Network address - The address by which we refer to the network
  All host bits are 0
Broadcast address - A special address used to send data to all hosts in the network
  All host bits are 1
Host addresses - The addresses assigned to the end devices in the network
  From all-zeroes to all-ones
Network prefix: the number of bits in the address that gives us the network portion

## Slide 46: Binary-decimal/octet conversion

## Slide 47: Network and host part
The network portion bits of the address - identical for all devices that reside in the same network.

## Slide 48: Netmask
Defines the size of the network part
  1…10…0
  The 1s in the subnet mask represent the network portion; the 0s represent the host portion

## Slide 49: Network prefixes

## Slide 50: 172.16.20.0/25

## Slide 51: Identify network address - ANDing

## Slide 52: Assigning IP addresses in a LAN
Static – manual
Dynamic - DHCP

## Slide 53: Communication
Unicast - one host to one host
  Typical communication
Broadcast - one host to all hosts in the network
  Directed – can be used remotely – using the broadcast address
  Limited – local network – using the 255.255.255.255 address
Multicast - one host to a selected group of hosts
  Reduce overall bandwidth (one packet for all listening hosts)
  Multicast clients subscribe to a group
  Uses (reserved) addresses: 224.0.0.0 – 239.255.255.255

## Slide 54: Reserved IP ranges
Multicast (RFC1700)
  224.0.0.0 – 239.255.255.255
Experimental: (RFC1700, RFC3330)
  240.0.0.0 – 255.255.255.254
Private/Network Address Translation (RFC1918)
  10.0.0.0 to 10.255.255.255 (10.0.0.0 /8)
  172.16.0.0 to 172.31.255.255 (172.16.0.0 /12)
  192.168.0.0 to 192.168.255.255 (192.168.0.0 /16)
Link local
  169.254.0.0 to 169.254.255.255 (169.254.0.0/16)
Test-net (teaching/learning)
  192.0.2.0 to 192.0.2.255 (192.0.2.0/24)

## Slide 55: Special IPv4 addresses
Network and broadcast addresses
  All-zeroes and all-ones host bits
Default route
  0.0.0.0
Loopback
  127.0.0.1

## Slide 56: Legacy IP addressing

## Slide 57: Network address planning
Criteria:
  Preventing duplication of addresses
  Providing and controlling access
  Monitoring security and performance
Allocation
  Static – manual
    Servers and routers
  Dynamic – automatic
    Using DHCP

## Slide 58: Assigning IP addresses
Level 0: the Internet - IANA
Level 1: Regional Internet Registries
Level 3: ISPs
Level 4: Network administrators

## Slide 59: Internet tiers

## Slide 60: Subnet mask
Defines the network and host portions

## Slide 61: Applying the subnet mask – ANDing

## Slide 62: ANDing example
Network address for host 172.16.132.70/20

## Slide 63: Ping and traceroute
Loopback
Local network
Remote device
Traceroute
  Sends packets with increasing TTL values
  Forces time exceeded replies from routers along the route

## Slide 64: Activities
5.1.6 / 5.1.7 – Binary-decimal conversion
https://learningcontent.cisco.com/games/binary/index.html
11.1.7 - ANDing to Determine the Network Address